## Slide 1: Readiness for RF capture
Cavities
  all 16 cavities commissioned with RF feedback loops closed
    klystron polar loop still to commission on 2 cavities
    2 lines somewhat unstable at 2MV
    more measurements needed this week
  reliability tests ongoing
    all cavities were run overnight at 2MV with Q=60000, Klystron power ~185kW
    some cavities tripped due to He pressure spike (magnet quench), 1 trip due to bad contact
Cavity phasing
  “quick” procedure established, avoids 16x access in RF zone
  cable measurements done last week & phase offsets calculated
  assume cable lengths inside modules are equal (~1mm)

## Slide 2: RF Low-Level system layout (simplified)
Notes: Cavity controller: feedback loops to control phase and amplitude in the cavity
  reduce the cavity impedance by factor 100
  very fast: RF feedback loop delay ~ 600 ns
Beam control: loops around the beam (phase, radial & synchro loops), frequency program
  slow: updates once per turn (11 kHz)
RF synchronization: between rings, and bunch-into-bucket transfers from SPS

## Slide 3: Readiness for RF capture
Beam control
  Beginning of next week, BC equipment (phase and synchro loops) will be installed and commissioned in SR4
    priority for this week is cavity optimisation
  Radial loop not needed for first beam (used during ramp)
Diagnostics
  Injection mountain range available via OASIS
  Initial commissioning done in SR4 using analogue signals
    frequency slip
    delays setup for beam phase sampling, etc.
    trigger initially on beam then on frev + delay
  Video connection to CCC for longitudinal pickup from scope in SR4
  Additional signals (peak detected pickup) via OASIS or 2nd video channel