## Slide 1: Injection Test Meeting Tuesday 26th August Controls Issues/Results Injection Kickers
Etienne CARLIER
AB/BT

## Slide 2
Injected BCT
  BCT signal now OK (~15mv for 2E+09)
  Still common mode noise between BI and BT racks during kicker MAIN switches turn-on
  Try to reject noise with passive filter and/or better ground separation between BI and BT
Softstart
  Some initial conditions not yet taken into account when ONSTANDBYSOFTSTART is performed (primary capacitor bank voltage to high w.r.t. requested start secondary voltage)
  ConditioningIsValid timer is restarted when RCPS is pulsed and not only when we have current in the magnet… ConditioningIsValid is restarted if the injection prepulse is missing
Injection kick (i.e. current in magnet) UTC timestamp
  Information available in MKI CTRVs when current in MKIMA.D5R8 or MKIMA.D5L2 is detected. Not clearly visible in application GUI and in logging database
  Add “xpocData” property within LhcMKIkick class with last valid injection kick data (UTC timestamp, settings, measures…)

## Slide 3
RBAC
  Unexpected (…unwanted) implementation of some RBAC features after a reboot of MKI FECs (i.e. no code modification)
  Full implementation under progress (FESA2.9/RDA2.4)
  Roles and Rules still to be created and tested
Logging
  MKIMA vacuum data logged into measurement and logging databases
  Data reduction still to be optimized
MKI GUI
  Some “space” for improvements
    Timing enable/disable control
    SOFTSTART duration monitoring
Injection Permit
  Seems OK
  BIS windows set to OK simultaneously for both injection kickers during interleaved injection operation
  Monitoring in OASIS is OK

## Slide 4
Timing
  Slow and Fast timing distribution (i.e. kicker pulsing) even with NO INJECTION REQUEST from the Sequencer
Inject and Dump
  Adjusted for BEAM2… it should be possible to dump the beam after ¼ turn. Still to be done for BEAM1
  Frev / Prepulse synchronisation should not be changed (i.e. prepulse should be received before Frev at pt6) otherwise it will not work anymore
  OASIS signals deployed for LBDS (B1/B2)
Lost of synchronisation for BEAM1 injection (-4us)
  Should not be linked to adjustment of “Inject and Dump” for BEAM2
  Reason(s) not yet understood
Fine synchronization of kicker magnet current
  Still to be done
Kick / Beam synchronization policy still to be defined
  BT kick delay Vs RF Bucket Selector